## Slide 1
COMPUTER COMMUNICATION & NETWORKS
Why We Got the
Internet Wrong
— and What NDN Is Trying to Fix
Named Data Networking | A New Internet Architecture
Presenters: Hamza Khan | Muhammad Saqib

## Slide 2
AGENDA
What We'll Cover Today
01
The Internet's Original Design
Where it came from and what it was built for
02
The Fundamental Mismatch
Why today's internet is broken by design
03
What Is NDN?
Named Data Networking — the core idea
04
How NDN Works
Packets, FIB, PIT, CS — the mechanics
05
NDN vs TCP/IP
Head-to-head comparison
06
Benefits & Applications
Security, efficiency, resilience
07
Challenges & Current Status
What's still unsolved
08
The Road Ahead
Future prospects & research

## Slide 3
THE ORIGIN
How the Internet Was Built
1969
ARPANET
4 nodes — UCLA, Stanford, UCSB, Utah. First packet switched network.
1974
TCP/IP
Cerf & Kahn design the protocol. Connects separate networks together.
1983
Internet
ARPANET adopts TCP/IP. The modern internet is born.
“Flag Day: networks of networks”.
1991
WWW
Tim Berners-Lee at CERN. Content sharing over HTTP explodes.
2024
Today
5.4 billion users. 500 hours of YouTube/min. Streaming dominates.
💡 Key Insight: The internet was designed to connect machines (endpoints) — not to distribute content. That design assumption is now 50 years old.
IMP: Internet Message Processors
NCP: Network Control Program (host machine).
NCP predecessor to TCP/IP.
Link different networks (like radio, satellites, and ground networks)
1974: published paper “A protocol for Packet Network Intercommunication”
1977: Three-Network Experiment. (Radio (Packet RadioNet), satellite (Atlantic SATNET), destination (data traveled through space and reached to the destination)
1989: Tim Berners-Lee invented www in 1989.
Internet vs web: Internet(Global network), Web(collection of multimedia page, links and documents). Hypertext: clickable text that jumps to another document. Berners-Lee invented three building blocks: HTML, HTTP, URL. Inshort, he wrote the world’s very first Web Browser and setup the world’s first website hosted on his NexT computer at CERN.

## Slide 4
THE PROBLEM
The Fundamental Mismatch
DESIGNED FOR
Machine-to-machine comms
Military & research networks
Reliable host-to-host delivery
Static, small-scale topology
Trusted, known endpoints
ACTUALLY USED FOR
Streaming video & music
Social media content delivery
Billions of simultaneous users
Mobile & dynamic networks
Untrusted, anonymous access
≠
Result: We patch a 1960s architecture with CDNs, NAT, VPNs, HTTPS — duct tape on a broken foundation.

## Slide 5
KEY FAILURES
What's Broken in TCP/IP Today
Address-Centric Naming
You ask WHERE content lives, not WHAT you want. If a server moves or goes down — connection broken.
Security as an Add-on
TLS/SSL were bolted on decades later. Internet was not designed with security; it's a perennial afterthought.
No In-Network Caching
Same Netflix video fetched millions of times from the same origin server. Massive bandwidth waste.
Mobility is Painful
IP addresses are location-bound. Moving between networks breaks TCP connections — NAT is a hack.
Scalability Limits
Routing tables are exploding. The global BGP table has >900,000 prefixes. IPv4 exhausted in 2011.
Multipath Inefficiency
TCP uses one path. If it fails, the whole session restarts. Parallel paths are wasted.

## Slide 6
THE SOLUTION
Named Data Networking (NDN)
"Instead of asking: WHERE is the data?
NDN asks: WHAT is the data?"
Origin
Proposed by Van Jacobson (Google / PARC) in 2009. Evolved from CCN — Content-Centric Networking.
Core Idea
Content is named, not addressed by location. Routers understand and cache content natively.
Security
Every piece of data is cryptographically signed at origin. Trust is in the data, not the channel.
NSF Project
U.S. National Science Foundation funds NDN as a Future Internet Architecture since 2010.

## Slide 7
ARCHITECTURE
How NDN Works — The Mechanics
TWO PACKET TYPES
Interest Packet
Consumer broadcasts: "I want /ndn/edu/video/lecture1"
Routers forward toward potential sources.
Data Packet
Producer replies with the named, signed data.
Routers cache it. Anyone nearby benefits.
EVERY NDN ROUTER HAS
FIB
Forwarding Information Base
Maps name prefixes to interfaces. Like a routing table but for names.
PIT
Pending Interest Table
Tracks outstanding Interests. Ensures Data travels back the same path.
CS
Content Store
In-router cache. If the data is already here — answer immediately. No origin needed.

## Slide 8
FLOW
NDN Request-Response Flow
Consumer
Router A
(CS miss)
Router B
(CS miss)
Producer
→
→
→
Interest: /ndn/edu/video/lecture1
←
←
←
Data: signed content packet travels back, cached at each router
🔄 Next user who requests the same content gets it from Router A or B's cache — producer never contacted again.

## Slide 9
NAMING
Hierarchical Content Names
TCP/IP:
http://server.edu/video/lecture1.mp4
Encodes server location. Content is tied to an address.
NDN:
/edu/university/video/lecture1/v1/seg0
Encodes WHAT the data is. Hierarchical, routable, location-independent.
Human-readable
Names describe content semantically — no cryptic IP addresses.
Aggregatable
Routers can aggregate /edu/* into one routing entry — scales well.
Location-agnostic
Content can be served from any router holding a cached copy.
Versioned
Versions and segments embedded in name — enables multipath fetch.

## Slide 10
COMPARISON
NDN vs TCP/IP — Head to Head
TCP/IP
NDN
What you request
An IP address + port
A content name
Security model
Secure the channel (TLS)
Secure the data itself (signatures)
Caching
Only at CDN edge servers
Every router caches content
Mobility
Connection breaks on IP change
Interest continues regardless of path
Multicast
Application-layer workaround
Built-in — same Interest fetches from cache
Routing basis
Destination IP address
Named content prefix
Trust model
Trust the server/channel
Trust the signed data object

## Slide 11
BENEFITS
Why NDN Is Better — Key Advantages
Built-in Security
Data is signed by producer at creation. Authentication is in the data — no channel trust needed. Prevents man-in-the-middle attacks at the data level.
In-Network Caching
Routers cache popular content. Reduces bandwidth consumption dramatically. ISPs save transit costs. Users get lower latency.
Better Scalability
Name aggregation keeps routing tables manageable. No IPv4/IPv6 exhaustion. Multicast is native — one copy serves many.
True Mobility
No IP-address dependency means seamless handoff between WiFi, 4G, 5G. Interest packets follow content regardless of path changes.
Resilience
Multiple paths simultaneously. No single point of failure. Works even under congestion — can pull from caches mid-route.
IoT & Edge Ready
Low-resource devices can participate. Named data works perfectly for sensor streams, vehicle networks, smart grids.

## Slide 12
USE CASES
Where NDN Shines — Applications
Video Streaming
Netflix/YouTube-style: cached at ISP router — no CDN needed. Viewers get content from nearest cache.
Vehicular (V2X)
Cars share traffic/road data by name. No IP setup overhead. Critical for autonomous driving networks.
Smart Grid & IoT
Sensor data named by location/time. Aggregated in-network. No central server bottleneck.
Healthcare IoT
Patient data named & signed. Privacy preserved. Works even when hospital network is disrupted.
Disaster Recovery
NDN routers work without central coordination. Data spreads through any available path — survivable.
CDN Replacement
ISPs can natively cache popular content — no need for Akamai/Cloudflare. Simpler, cheaper, faster.

## Slide 13
CHALLENGES
Unsolved Problems & Obstacles
!
Naming at Scale
Who controls the namespace? No global naming authority exists yet. Risk of naming conflicts across organizations.
!
Router Memory Cost
Content Store (cache) requires significant RAM/storage at every router. Hardware upgrades needed globally.
!
Interest Flooding
Malicious actors can flood the network with Interests — a new DDoS vector unique to NDN. Defenses still evolving.
!
Backward Compatibility
Internet's trillion-dollar infrastructure runs TCP/IP. Wholesale replacement is not feasible. Transition is complex.
!
Privacy Concerns
Named data means routers can see what content users request. More visibility than IP packets (which only show endpoints).
!
Deployment Incentives
Who pays for the upgrade? ISPs need economic incentive to deploy NDN routers. No global governance mechanism yet.

## Slide 14
STATUS
Where NDN Stands Today
KEY MILESTONES
2009
Van Jacobson publishes CCN paper at Google Tech Talk
2010
NSF awards Future Internet Architecture grant to NDN project
2013
NDN testbed deployed across U.S. university campuses
2016
NDN-over-WiFi demonstrated for V2X automotive networks
2018
NFD (NDN Forwarding Daemon) v0.6 released — open source
2020
NDN deployed in smart grid and healthcare IoT pilots
2024
Active research in 30+ institutions worldwide
ACTIVE RESEARCH AREAS
NDN Testbed
Live experimental network connecting 30+ institutions globally
ndn-cxx / NFD
Open-source C++ library & forwarder — anyone can run NDN
NLSR
NDN Link State Routing Protocol — routing for NDN networks
Named Data Link Layer Protocol (NDNLP)
Adapts NDN to physical links
ChronoSync
Distributed dataset sync over NDN — shared state without servers
Trust Schema
Formal language for specifying NDN trust and key hierarchies

## Slide 15
FUTURE
The Road Ahead for NDN
Overlay Networks
NDN runs ON TOP of existing IP infrastructure — gradual coexistence. Most likely near-term path. Tunneled NDN over UDP/IP.
Hybrid Future
Specific sectors adopt NDN natively: automotive networks, smart cities, IoT. Parallel internet architectures for different use cases.
Clean Slate Internet
Long-term: NDN replaces IP as the universal internet layer. Requires global policy coordination. Decades away — but theoretically superior.
Near-term
Mid-term
Long-term
NDN won't replace the internet overnight — but it is the most rigorous rethink of internet architecture since TCP/IP.

## Slide 16
SUMMARY
Key Takeaways
01
The internet was designed to connect machines — not deliver content. That design is 50 years old.
02
TCP/IP forces you to ask WHERE content is. NDN asks WHAT you want — a fundamental paradigm shift.
03
NDN routers cache content natively: FIB routes Interest packets, PIT tracks pending requests, CS stores data.
04
Security is in the data itself via cryptographic signatures — not bolted on the channel.
05
NDN enables native multicast, mobility, resilience, and scalability without CDNs or NAT.
06
Challenges remain: naming governance, router memory, privacy, and the trillion-dollar deployment barrier.
07
NDN is actively funded, open-sourced, and deployed in testbeds — it's research, not just theory.

## Slide 17
Thank You
Questions & Discussion
"The best way to predict the future of the internet is to invent it."
Reference: named-data.net | Van Jacobson, 2009 — "Networking Named Content"