## Slide 1: OSI Transport Layer
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
١

## Slide 2: Objectives
٢
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Explain the role of Transport Layer protocols and services in supporting communications across data networks
Analyze the application and operation of TCP mechanisms that support reliability, reassembly and manage data loss.
Analyze the operation of UDP to support communicate between two processes on end devices

## Slide 3: Transport Layer Role and Services
٣
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
The purpose of the Transport layer

## Slide 4: Transport Layer Role and Services
٤
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Provides the end-to-end transfer of data between applications.

## Slide 5: Role of the Transport layer
٥
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Encapsulating application data for use by the Network layer
Enables multiple applications to communicate over the network at the same time on a single device
Ensures that, if required, all the data is received reliably and in order by the correct application
Error handling mechanisms

## Slide 6: Responsibilities
٦
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Tracking the individual communication between applications on the source and destination hosts (Establishing a Session )
Segmenting data and managing each piece
Reassembling the segments into streams of application data
Identifying the different applications (Port Number)

## Slide 7: Two TCP/IP Transport layer protocols
٧
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
  There are multiple Transport layer protocols. Why?
  Because different applications have different requirements.

## Slide 8
٨
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
The two most common
Transport layer protocols of TCP/IP protocol suite are Transmission Control Protocol (TCP)
User Datagram Protocol (UDP).
Both protocols manage the communication of multiple applications.
The differences between the two are the specific functions that each protocol implements.
Two TCP/IP Transport layer protocols

## Slide 9: TCP/IP Transport layer protocols: TCP and UDP.
٩
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
TCP at the Transport layer provide:
Connection-oriented conversations
Reliable delivery
Ordered data reconstruction
Flow control

## Slide 10: Basic characteristics of the UDP and TCP Protocols
١٠
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
UDP Protocol
Fast
Low overhead
Does not require acknowledgements
Does not resend lost data
Delivers data as it arrives
TCP Protocol
-Reliable
Acknowledges data
Resends lost data
Delivers data in the order sent

## Slide 11: Transport Layer Role and Services
١١
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Supporting Reliable Communication

## Slide 12
١٢
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
UDP
UDP is a simple, connectionless protocol
Low overhead data delivery.
Datagrams are sent as "best effort" by this Transport layer protocol.

## Slide 13: Applications that use UDP include:
١٣
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Domain Name System (DNS)
Video Streaming
Voice over IP (VoIP)

## Slide 14: Transmission Control Protocol (TCP)
١٤
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Connection-oriented protocol,
Overhead
Flow control

## Slide 15: Applications that use TCP are:
١٥
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Web Browsers
E-mail
File Transfers

## Slide 16: Transport Layer Headers
١٦
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Segment or datagram?

## Slide 17: Port Number, Identifying the Conversations
١٧
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Port numbers are assigned in various ways,
Depending on whether the message is a request or a response.
Server processes have static port numbers assigned to them.
Clients dynamically choose a port number for each conversation.

## Slide 18: Port Number
١٨
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
When a client application sends a request to a server application,
The destination port contained in the header is the port number that is assigned to the service daemon running on the remote host.
The client software must know what port number is associated with the server process on the remote host.
This destination port number is configured, either by default or manually.
For example, when a web browser application makes a request to a web server, the browser uses TCP and port number 80 unless otherwise specified. This is because TCP port 80 is the default port assigned to web-serving applications.

## Slide 19
١٩
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
The combination of the Transport layer port number and the Network layer IP address assigned to the host uniquely identifies a particular process running on a specific host device.
This combination is called a socket.
192.168.1.20:80.
Socket & Port Number

## Slide 20: Data Delivery Based on Port Number
٢٠
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 21: There are different types of port numbers:
٢١
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Well Known Ports (Numbers 0 to 1023)
These numbers are reserved for services and applications.
They are commonly used for applications such as HTTP (web server) POP3/SMTP (e-mail server) and Telnet.
  IANA (Internet assigned numbers authority)
Registered Ports (Numbers 1024 to 49151)
These port numbers are assigned to user processes or applications.
These processes are primarily individual applications that a user has chosen to install rather than common applications that would receive a Well Known Port.
These ports may also be used dynamically selected by a client as its source port.

## Slide 22
٢٢
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Dynamic or Private Ports (Numbers 49152 to 65535)
These numbers are usually assigned dynamically to client applications when initiating a connection.

## Slide 23: Using both TCP and UDP
٢٣
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Some applications may use both TCP and UDP.
For example, the low overhead of UDP enables DNS to serve many client requests very quickly.
However Sometimes, sending the requested information may require the reliability of TCP.
In this case, the well known port number of 53 is used by both protocols with this service.

## Slide 24: TCP Ports
٢٤
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 25: UDP Ports
٢٥
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 26: Netstat
٢٦
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Netstat provides information and statistics about protocols in use and current TCP/IP network connections and Port numbers.
(The name derives from the words network and statistics.)
For details
http://searchnetworking.techtarget.com/definition/netstat

## Slide 27: TCP Segments
٢٧
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Dividing application data into pieces both ensures that data is transmitted within the limits of the media and that data from different applications can be multiplexed on to the media.

## Slide 28: Segments
٢٨
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 29: TCP Segment Header
٢٩
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 30: Application and Operation of TCP Mechanisms
٣٠
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Port numbers in establishing TCP sessions and directing segments to server process

## Slide 31: TCP Connection Establishment and Termination
٣١
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
When two hosts communicate using TCP, a connection is established before data can be exchanged.
After the communication is completed, the sessions are closed and the connection is terminated.
The connection and session mechanisms enable TCP's
reliability function.

## Slide 32: Handshake in the establishment of TCP sessions
٣٢
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 33: Handshake in the termination of TCP sessions
٣٣
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 34
٣٧
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
The sequence number is the relative number of bytes that have been transmitted in this session plus 1.
Acknowledgement number indicate the next byte in this session that the receiver expects to receive.

## Slide 35: Managing TCP Sessions
٣٨
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
TCP sequence numbers are used to reconstruct the data stream with segments placed in the correct order

## Slide 36: Managing TCP Sessions
٣٩
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Trace the steps used by the TCP protocol in which sequence numbers and acknowledgement numbers are used to manage exchanges in a conversation

## Slide 37
٤٠
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
The amount of data that a source can transmit before an acknowledgement must be received is called the window size.
Window Size is a field in the TCP header that enables the management of lost data and flow control.
Sliding window refers to the fact that the window size is negotiated dynamically during the TCP session
Window Size

## Slide 38: TCP Windows and Flow Control
Data often is too large to be sent in a single segment. TCP splits the data into multiple segments.
TCP provides flow control through “windowing” to set the pace of how much data is sent at a time – IE how many bytes per window, and how many windows between ACKs.
Window Size = 1
Window Size = 3

## Slide 39: TCP Retransmission
٤١
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
For example,
If segments with sequence numbers 1500 to 3000 and 3400 to 3500 were received, the ack number would be 3001.
This is because there are segments with the sequence numbers 3001 to 3399 that have not been received.
When TCP at the source host has not received an ack after a predetermined amount of time, it will go back to the last acknowledgement number that it received and retransmit data from that point forward.

## Slide 40: Flow Control
٤٢
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Window size, and congestion during a session

## Slide 41: Flow Control
If the source receives no acknowledgment, it knows to retransmit at a slower rate.
Fast enough for you?
I didn’t get all of that, slow down.

## Slide 42: UDP Protocol
٤٣
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 43
٤٤
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
UDP is a simple protocol that provides the basic Transport layer functions.
It has a much lower overhead than TCP, since it is not connection-oriented and does not provide the sophisticated retransmission, sequencing, and flow control mechanisms.
UDP Protocol

## Slide 45
٤٥
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Key Application layer protocols that use UDP include:
Domain Name System (DNS)
Simple Network Management Protocol (SNMP)
Dynamic Host Configuration Protocol (DHCP)
Routing Information Protocol (RIP)
Trivial File Transfer Protocol (TFTP)
Online games
UDP Protocol

## Slide 46: UDP Reassembles
٤٦
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
UDP does not keep track of sequence numbers the way TCP does.
UDP has no way to reorder the datagrams into their transmission order.
UDP simply reassembles the data in the order that it was received and forwards it to the application.
If the sequence of the data is important to the application, the application will have to identify the proper sequence of the data and determine how the data should be processed.

## Slide 47: UDP Protocol
٤٧
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 48: UDP Protocol – Port Number
٤٨
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Servers use port numbers to identify a specified application layer process and direct segments to the proper service or application

## Slide 49: UDP Protocol
٤٩
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public
Trace the steps as the UDP protocol and port numbers are utilized in client-server communication.

## Slide 50: Denial of Service Attacks
Hacker initiates a SYN but spoofs the source IP address.
DoS attacks are designed to deny services to legitimate users.
DoS attacks are used by hackers to overwhelm and crash systems.
SYN flooding is a DoS attack that exploits the three way handshake.
To defend against these attacks, decrease the connection timeout period and increase the connection queue size. Software also exists that can detect these types of attacks and initiate defensive measures.
Send SYN
Receive SYN
Send SYN/ACK
Send SYN
Send SYN
Send SYN
Send SYN
Send SYN
Target replies to the unreachable IP address and waits for final ACK.
Hackers floods target with false SYN requests tying up its connection resources, preventing it from responding to legitimate connection requests.
Notes: One type of DoS is known as SYN flooding. SYN flooding exploits the normal three-way handshake and causes targeted devices to acknowledge to source addresses that will not complete the handshake.

## Slide 51: UDP Port Numbers
Echo 7 Echo user datagram back to user
Discard 9 Discard user datagrams
Daytime 13 Report time in a user friendly fashion
Quote 17 Return "Quote of the day"
Chargen 19 Character generator
Nameserver 53 Domain Name Server
Sql-Net 66 Oracle Sequel Network
BOOTPS 67 Server port to download configuration information
BOOTPC 68 Client port to receive configuration information
TFTP 69 Trivial File Transport Protocol
POP3 110 Post Office Protocol - V3
SunRPC 111 Sun Remote Procedure Call
NTP 123 Network Time Protocol
SNMP 161 Used to receive network management queries
SNMP-trap 162 Used to receive network problem reports.
IRC 194 Internet Relay Chat
IPX 213 IPX - IP Tunneling
SysLog 514 System Log
RIP 520 Routing Information Protocol
NFS 2049 Network File Service

## Slide 52: TCP vs UDP
TCP | UDP
Connection-oriented delivery | Connectionless delivery, faster
Uses windows and ACKs | No windows or ACKs
Full header | Smaller header, less overhead
Sequencing | No sequencing
Provides reliability | Relies on app layer protocols for reliability
FTP, HTTP, SMTP, and DNS | DNS, TFTP, SNMP, and DHCP

## Slide 53: Some Well-Known TCP Ports
9 Discard Discard all incoming data port
7 Echo Echo
19 Chargen Exchange streams of data port
20 FTP-Data File transfer data port
21 FTP-CMD File transfer command port
23 Telnet Telnet remote login port
25 SMTP Simple Mail Transfer Protocol port
53 DOMAIN Domain Name Service
79 Finger Obtains information about active users
80 HTTP Hypertext Transfer Protocol port
88 Kerberos Authentication Protocol
110 POP3 PC Mail retrieval service port
119 NNTP Network news access port
161 SMTP Network Management
179 BGP Border Gateway Protocol
513 Rlogin Remote Login In
Port Application Description

## Slide 54: Quiz
٥٠
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 55
٥١
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 56
٥٢
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 57
٥٣
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 58
٥٤
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 59
٥٥
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 60
٥٦
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 61
٥٧
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public

## Slide 62
٥٨
© 2007 Cisco Systems, Inc. All rights reserved.
Cisco Public