## Slide 1: Link-State Routing Protocols
Dr. Muazzam A. Khan

## Slide 2: Objectives
Describe the basic features & concepts of link-state routing protocols.
List the benefits and requirements of link-state routing protocols.

## Slide 3: Introduction

## Slide 4: Link-State Routing
Link state routing protocols
  -Also known as shortest path first algorithms
-These protocols built around Dijkstra’s SPF

## Slide 5: Link-State Routing
Dikjstra’s algorithm also known as the shortest path first (SPF) algorithm

## Slide 6: Link-State Routing
The shortest path to a destination is not necessarily the path with the least number of hops

## Slide 7: Link-State Routing
Link-State Routing Process
How routers using Link State Routing Protocols reach convergence
    -Each routers learns about its own directly connected networks
    -Link state routers exchange hello packet to “meet” other directly
    connected link state routers.
    -Each router builds its own Link State Packet (LSP) which includes information about neighbors such as neighbor ID, link type, & bandwidth.
    -After the LSP is created the router floods it to all neighbors who then store the information and then forward it until all routers have the same information.
    -Once all the routers have received all the LSPs, the routers then construct a topological map of the network which is used to determine the best routes to a destination

## Slide 8: Link-State Routing
Directly Connected Networks
Link
This is an interface on a router
Link state
This is the information about the state of the links

## Slide 9: Link-State Routing
Sending Hello Packets to Neighbors
Link state routing protocols use a hello protocol
Purpose of a hello protocol:
-To discover neighbors (that use the same link state routing protocol) on its link

## Slide 10: Link-State Routing
Sending Hello Packets to Neighbors
Connected interfaces that are using the same link state routing protocols will exchange hello packets.
Once routers learn it has neighbors they form an adjacency
-2 adjacent neighbors will exchange hello packets
-These packets will serve as a keep alive function

## Slide 11: Link-State Routing
Building the Link State Packet
Each router builds its own Link State Packet (LSP)
Contents of LSP:
-State of each directly connected link
-Includes information about neighbors such as neighbor ID, link type, & bandwidth.

## Slide 12: Link-State Routing
Flooding LSPs to Neighbors
Once LSP are created they are forwarded out to neighbors.
  -After receiving the LSP the neighbor continues to forward it throughout routing area.

## Slide 13: Link-State Routing
LSPs are sent out under the following conditions
-Initial router start up or routing process
-When there is a change in topology

## Slide 14: Link-State Routing
Constructing a link state data base
Routers use a database to construct a topology map of the network

## Slide 15: Link-State Routing

## Slide 16: Link-State Routing
Shortest Path First (SPF) Tree
Building a portion of the SPF tree
Process begins by examining R2’s LSP information
-R1 ignores 1st LSP
Reason: R1 already knows it’s connected to R2

## Slide 17: Link-State Routing
Building a portion of the SPF tree
-R1 uses 2nd LSP
Reason: R1 can create a link from R2 to R5. This information is added to R1’s SPF tree

## Slide 18: Link-State Routing
Building a portion of the SPF tree
-R1 uses 3rd LSP
      Reason: R1 learns that R2 is connected to 10.5.0.0/16.
      This link is added to R1’s SPF tree.

## Slide 19: Link-State Routing
Determining the shortest path
  The shortest path to a destination determined by adding the costs & finding the lowest cost

## Slide 20: Link-State Routing
Once the SPF algorithm has determined the shortest path routes, these routes are placed in the routing table.

## Slide 21: Link-State Routing Protocols
Routing protocol | Builds Topological map | Router can independently determine the shortest path to every network. | Convergence | A periodic/ event driven routing updates | Use of LSP
Distance vector | No | No | Slow | Generally No | No
Link State | Yes | Yes | Fast | Generally Yes | Yes
Advantages of a Link-State Routing Protocol

## Slide 22: Link-State Routing Protocols
Requirements for using a link state routing protocol
Memory requirements
Typically link state routing protocols use more memory
Processing Requirements
More CPU processing is required of link state routing protocols
Bandwidth Requirements
Initial startup of link state routing protocols can consume lots of bandwidth

## Slide 23: Link-State Routing Protocols
2 link state routing protocols used for routing IP
-Open Shortest Path First (OSPF)
-Intermediate System-Intermediate System (IS-IS)

## Slide 24: Summary
Link State Routing protocols are also known as Shortest Path First protocols
Summarizing the link state process
-Routers 1ST learn of directly connected networks
-Routers then say “hello” to neighbors
-Routers then build link state packets
-Routers then flood LSPs to all neighbors
-Routers use LSP database to build a network topology map & calculate the best path to each destination

## Slide 25: Summary
Link
An interface on the router
Link State
Information about an interface such as
-IP address
-Subnet mask
-Type of network
-Cost associated with link
-Neighboring routers on the link

## Slide 26: Summary
Link State Packets
After initial flooding, additional LSP are sent out when a change in topology occurs
Examples of link state routing protocols
-Open shortest path first
-IS-IS